## Slide 1
NATIONAL DISASTER MANAGEMENT AUTHORITY
From Flood Simulation to
Decision Support
A Digital Twin Pathway for Critical Infrastructure Resilience
Kalpani River Basin · Proof of Concept
Presenter Name · Wing / Directorate · 8 September 2026

## Slide 2
WHY THIS MATTERS
The Cost of Not Knowing in Advance
Pakistan Floods 2022 — Post-Disaster Needs Assessment
$5.6B
Housing sector damage
plus $636M in ongoing economic losses
780,000
Homes destroyed outright
1.27 million more damaged, left standing
13%
of health facilities disrupted
service delivery interrupted nationwide
Source: Pakistan Floods 2022 — Post-Disaster Needs Assessment. Govt. of Pakistan · Asian Development Bank · European Union · UN agencies · World Bank (Oct 2022)
02

## Slide 3
THE CORE IDEA
From Reactive to Anticipatory
What “Digital Twin” Means Here
A digital twin: a live, data-driven replica of a river basin that behaves like the real one under any rainfall you throw at it
Not a map — a model that computes how water moves, where it pools, and what it touches
Purpose: turn “what happened” into “what if” — the same kind of scenario discussion NDMA already runs in tabletop exercises, grounded in physics and real terrain instead of assumption
Physical Basin
Live Digital Replica
Same terrain. Same physics. Any rainfall you ask it.
03

## Slide 4
PROOF OF CONCEPT
What We Built: A Working Proof of Concept
Kalpani River basin (Mardan / Nowshera) — full hydrodynamic simulation, not a sketch
Terrain from FABDEM, a bare-earth global elevation dataset — removes the building/canopy noise that corrupts cheaper elevation data
Every rainfall scenario is real data — historic recorded events or statistically derived from 44 years of satellite rainfall record — zero assumed numbers
Output: an interactive dashboard showing flood depth, extent, and exposed buildings, scenario by scenario
Kalpani Flood Risk Platform
Peak Depth 0.1–4m
SCENARIOS
5 Aug 2006
2010 event
P50 day
P75 day
P90 day
T25 storm
Illustrative interface — live demonstration follows
04

## Slide 5
CREDIBILITY
Validated Against Real History, Not Just Theory
5 AUGUST 2006
Kalpani bridge collapse, Mardan
Discharge: 2,285–2,597 m³/s
field reading vs. independent hydraulic reconstruction agree within ~12%
VALIDATION EVENT
JULY 2010
Nationwide monsoon flood
Discharge up to 3,361 m³/s
largest recorded discharge on the Kalpani in the literature
CALIBRATION / STRESS-TEST
Source: Ullah, Farooq, Sarwar, Tareen & Wahid (2016), Arabian Journal of Geosciences 9(6); DAWN, 6 Aug 2006
05

## Slide 6
LIVE DEMONSTRATION
Scenario Selection → Depth & Extent → Building Exposure
Backup recording available if connectivity fails
06

## Slide 7
THE CAPABILITY
What the Model Already Tells Us
Every scenario below is real — a recorded historic event, or derived directly from 44 years of satellite rainfall records for this exact watershed.
Chart: Rainfall total, mm (each scenario's full rainfall window)
| Ordinary day (P50) | Notable day (P75) | Minor-flood threshold (P90) | Illustrative day, 2011 | 2006 event · historic | T5 design storm | T10 design storm | T25 design storm | T50 design storm | T100 design storm | 2010 event · historic
Rainfall total (mm) | 7.9 | 18.3 | 33.9 | 75.3 | 81.8 | 82 | 95 | 112 | 124 | 137 | 202.4
Source: CHIRPS Daily (UCSB-CHG), GPM IMERG V07, PMD — basin-mean totals computed for this exact watershed polygon
07

## Slide 8
SPEAKING PLAINLY
Today's Honest Limit
What It Does Today
Computes real flood depth and extent per scenario — a physics-based hydrodynamic solve, not an estimate
Validated against two real, independently-corroborated historic events (2006, 2010)
Joins simulated depth to real building footprints for an exposure count, scenario by scenario
What It Doesn't — Yet
Doesn't yet put a rupee figure on the damage — no cost-of-repair estimate
Doesn't yet distinguish building vulnerability by construction type or material
Building layer currently mismatched to the final watershed boundary — disclosed, not hidden
Why: a defensible cost figure requires knowing what a building is made of — not just where it stands.
08

## Slide 9
THE NEXT CAPABILITY
The Missing Link: Material Data (BIM)
BIM — Building Information Modeling — a structured digital record of what a building is actually built from
Depth
+
Velocity
+
Duration
+
Material
(BIM)
Defensible
Cost of Damage
Not a novel technique — this is the same depth-damage curve method used in FEMA's HAZUS flood-loss model, a methodology referenced globally, including in World Bank-funded work.
Source: FEMA Hazus 5.1 Flood Model Technical Manual
09

## Slide 10
THE OVERLOOKED COST
Damage Isn't Just What You Can See
PEAK FLOOD LEVEL
Electrical systems
Wiring, panels, outlets — damage begins in the first few inches of water
Plumbing & drainage
Sanitation and drainage lines contaminated and corroded
Contents & finishes
Flooring, furnishings, fixtures — replaced, not repaired
International flood-damage methodology (FEMA / USACE) treats interior systems as standard, quantifiable damage — not an afterthought. Damage to electrical systems can begin before water is even visible at the door.
Source: FEMA Hazus 5.1 Flood Model Technical Manual; USACE depth-damage functions — npj Natural Hazards (2024)
10

## Slide 11
WHERE TO START
Why Public Infrastructure Comes First
Hospitals
Continuity of care
Schools
Community shelters
Warehouses
Emergency supply chains
Power & Water
Lifeline services
A flooded warehouse is an inventory loss. A flooded hospital is a capability loss — at the exact moment it's needed most.
13% of Pakistan's health facilities were disrupted in the 2022 floods — Pakistan Floods 2022 PDNA
11

## Slide 12
FROM MODEL TO ACTION
From Simulation to Decision: The Value Chain
1
IDENTIFY
Which critical infrastructure sits in a real, modeled hazard zone
2
PRIORITIZE
Rank those assets by modeled exposure severity
3
GUIDE
Steer future development away from high-hazard zones
4
AUDIT
Turn the ranked list into a standing inspection schedule
12

## Slide 13
THE VISION
The Bigger Picture: A Digital Twin Ecosystem
KALPANI
(proven)
Basin B
Basin C
Basin D
Basin E
Kalpani is one basin — proof that the method works
Same pipeline is basin-agnostic — extendable nationally, watershed by watershed
End state: a living, continuously-updated national flood digital twin feeding a standing decision-support system
13

## Slide 14
THE ASK
What's Needed to Get There
Material Data (BIM)
Building-level construction data — starting with critical infrastructure first, not full national coverage at once
Rainfall & Discharge Access
Continued access to real records via PMD's Climate Data Processing Centre — a relationship worth formalizing
A Standing Mandate
Run this as an operational tool that gets used and updated — not a one-time study filed away
14

## Slide 15
“A digital twin doesn't predict the future —
it lets you rehearse it.”
The infrastructure is real. The rainfall is real. The physics is real.
Questions & Continued Demo
Presenter Name · Wing / Directorate · rameen.arsalan369@gmail.com
15

## Slide 16
APPENDIX · BACKUP SLIDE
Build Methodology at a Glance
Shown only if asked — the full stage-by-stage build log lives in the master plan document.
1
Terrain
(FABDEM)
2
Watershed
Delineation
3
Land Cover /
Soil / Roughness
4
Rainfall
Forcing
5
Hydrodynamic
Solve (SFINCS)
6
Peak Depth
& Velocity
7
Building
Exposure
Every input is real-data-only: FABDEM (bare-earth terrain), ESA WorldCover, SoilGrids, CHIRPS/GPM IMERG rainfall, KP Irrigation Dept. cross-sections where obtainable — no assumed or indicative values anywhere in the pipeline.
16

## Slide 17
APPENDIX · BACKUP SLIDE
Sources & References
Data Sources
FABDEM V1-2 — Univ. of Bristol / Fathom
CHIRPS Daily — UCSB Climate Hazards Group
GPM IMERG V07 — NASA
ESA WorldCover 10m v200
SoilGrids 250m — ISRIC
Model Validation
Ullah, Farooq, Sarwar, Tareen & Wahid (2016), Arabian J. of Geosciences 9(6)
DAWN, 6 Aug 2006 — Mardan bridge collapse report
Damage Methodology
FEMA Hazus 5.1 Flood Model Technical Manual
USACE depth-damage functions — npj Natural Hazards (2024)
FEMA P-348, Protecting Building Utility Systems From Flood Damage
National Context
Pakistan Floods 2022 PDNA — Govt. of Pakistan, ADB, EU, UN agencies & World Bank
World Bank / GFDRR — disaster loss estimation methodology
17